## Slide 1: ConQuest: Queue Analysis in the Data Plane
Xiaoqi Chen, Shir Landau Feibish, Yaron Koral, Jennifer Rexford, Ori Rottenstreich, Steven A Monetti, Tzuu-Yi Wang

## Slide 2: Everyone hates…

## Slide 3: Everyone hates long queues… -
Notes: Today, talk about sth everyone hates.
We hate waiting half an hour for uber.
Uber: essentially waiting in a queue, too many passengers calling uber for a ride
I’m also angry when I was watching soccer game live streaming, and suddenly…
It’s also because long queues -- the queues in network routers.

## Slide 4: Queuing in routers
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Crossbar
Notes: Each network routers have ingress ports and egress ports.
After a packet comes in, we made some routing decisions (which egress port);
Then crossbar,
then there’s the queue before egress port. (This is output-queued device.)

## Slide 5: Queuing in routers
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Crossbar
Packet
Packet
Notes: Let’s for now focus on this simplified model, only one port, assume one FIFO queue on this port. other cases in paper
The queue is necessary for packet switches, as two packets may want to go to the same egress port.
We need it for statistical multiplexing.
Back in circuit switches, no queues…

## Slide 6: Long queues?
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Queue
Egress
Ingress
Routing
Crossbar
Packet
Packet
Packet
Packet
Notes: When too many packets come in, queueing buffer full.
Subsequent packet dropped.
Carries data for your live-streaming soccer game – rebuffer.
Even before dropping, long queues cause high delay. player for online games frustrated for “lags”.
End at 2:00?

## Slide 7: Long queues? Delay and jitter!
Bad for interactive applications
Microburst: sub-millisecond queuing
In data center networks (e.g., incast)
In carrier networks (unknown reason)
  Can’t use hosts to monitor/mitigate
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts
Notes: So, we know long queues are bad for interactive …
In particular, a phenomenon called uburst. If we plot qlen over time, sudden growth, within millisec.
Max qlen per second shown, 24 hr in total (explain)
Uburst exists in DCN, we know one of the cause, incast: many senders…
We can solve it by changing algo in app layer
But uburst also exists in carrier network! In fact, this figure comes from ATT carrier core, not expecting Ubursts in core.
Also, we don’t know the cause.
Unlike DCN, carrier network op can’t control end hosts, to monitor or mitigate...
We’re looking for solutions to analyze and mitigate ubursts at router
3:20

## Slide 8: Programmable switch to the rescue
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Traditional routers: limited visibility, coarse-grained stats
By the time you see microbursts, the harm is already done…
P4-enabled programmable switch allows real-time, fine-grained queue analysis
Microbursts
Notes:   traditional routers tie our hands
  1. Only queue length!
  2. Seconds or minutes granularity
Offline analysis, post-mortem, too late
(soccer live-steram watcher, online game player unhappy)
Online, real time reaction to microburst!
End at 4:00

## Slide 9: Why am I waiting?
Which flow has many packets in the queue?
Queue
Egress
A
B
B
C
E
D
B
B
Flow ID: A
{SrcIP: XXX, DstIP: YYY}
Why am I waiting?
B
It’s because flow B!
It’s because
the NBA game!
Why am I waiting?
Notes: Now it’s possible to answer:
Each packet belongs to certain application. Define flow ID.
…
… It may wonder ... A clever smurf can
Just like in uber case, smurf
although I'm a soccer fan, not a basketball fan, I still need to wait when many people called Uber ...
Knowing the answer: don't fly ... after the NBA game just finished (Golden State warrior).
Knowing the answer, a programmable switch may react immediately to mitigate the upcoming burst, e.g. by rerouting or de-prioritize packets from flow B.
Suppress microburst surgically!
So, lower queuing delay -> lower jitter, better video streaming.
Also, knowing flow B -> knowing which application, find root cause, change application
End at 5:00

## Slide 10: ConQuest: why am I waiting?
Notes: Today we present ConQuest, a data plane data structure which answers the question "why am I waiting".
However, it’s non-trivial to answer this question, even on a PSw.
at 5:20.

## Slide 11: A strawman solution
Flow | Count
Maintain a “flow size in the queue” table
Increment when packet arrives
Subtracts when packet exits
A
1
B
1
C
1
Queue
Egress
A
B
C
0
C
2
Memory access
Memory access
Notes: Let's look at this strawman solution. maintain a table
when packet arrives, inc count
to simplify, assume unit sized packet
another arrives, ...
6:30

## Slide 12: Challenge: memory partitioned!
100 Gbps = one packet per 6.7 nanoseconds
Concurrent access is hard to implement
  Need to prevent memory hazard
Memory partitioned before and after queuing
Queue
Egress
Packet
Shared Memory
Write
Write
Notes: in high-speed ..., not 1 pkt per second, but 100G means 6ns
- animation
so, simultaneous writes from both end, once per 6ns
Not impossible, but challenging and costly, hence on today’s PS arch it’s partitioned.
-> can’t simultaneous…
therefore, cannot maintain a shared table and inc/dec on ENqueue/DEqueue
End at 7:30

## Slide 13: Solution: snapshots
S1 | S2 | S3 | S4 | …
Memory access
Flow | ~Count
 | 1
 | 5
 | 1
 | 1
Slice traffic into time windows
Each snapshot records T=4 packets
Queue
Egress
B
E
Historical Departures
D
B
A
C
C
D
B
B
B
A
B
B
I enqueued at t=5
I dequeued at t=14
Why am I waiting?
?
A
B
C
D
Notes: ConQuest's solution to the arch challenge is to use snapshots to address the partitioned memory.
We split traffic into time windows, save into multiply snapshots
Example. Simplified, packet all same size, 1 pkt/sec.
Metadata: Every packet knows when did it …, how long did it waited
Note: how many to read: queue length / T
End at 9:30

## Slide 14: So far so good? Gotta reuse them
Each snapshot records a time window T of traffic (using sketch)
Write into one snapshot
Read recent snapshots
# snapshots to read = (max queuing delay)/T
Need cleaning every T ≤ 1ms
Control plane is too slow!
Notes: recap:
1. slice into T
2. write
3. when suffered from high queuing delay, read recent. divide delay by T.
end at 10:50

## Slide 15: Solution: round-robin snapshots
Clean and Reuse the snapshots in the data plane!
Read
Read
Write
Clean
Read
Read
Read
Notes: Our solution: clean and reuse fully within data plane.
Example, s3 being written
As packets get dequeued, write, also write 0 into s4
More packets, 0 in more locations
s3 full, s4 empty. Possible: use sketch in snapshots, #memory addresses i.e. zeros needed <= #pkts
End at 12:00

## Slide 16: The ConQuest data structure
Slice traffic into time windows
For each packet dequeued:
  Write into the latest snapshot
  Read some recent snapshots
  Clean the oldest snapshot
Notes: In summary, this is the ConQuest DS:
We use round-robin between several snapshots, each holding a sketch.
(In our impl uses CMS, can use other)
Slice traffic
for each:
write, into latest, corresponds to current time window
read, how many to read: queuing delay divided by T
clean, write some 0 to help cleaning the oldest snap
End at 12:50 is good?

## Slide 17: Evaluation

## Slide 18: Evaluation 1: is ConQuest accurate?
Python-based Simulator
Trace: UWISC IMC’10 data center
Find flows occupying >α queue
Metric: Precision & Recall, for finding large flows in queue during congestion
Result: >90% Precision & Recall
Notes: (Skip if no time.)
py sim: know ground truth of queuing, any time, any pkt
trace: public, burstiness
What alpha: fraction of queue, say 100 pkts in front, I specify 30%, so >30pkts is large flow.
Metric: precision / recall, for binary classifier. Precision relates to true positive, Recall relates to false positive, both are higher better.
They’re trade-off of each other, hence we plot the precision/recall curve (“AUPR”) . Area 92.5%
Mention: works well for all alpha range. Alpha relates to how many bursty flows you have in the system.
End at 14:20?

## Slide 19: Evaluation 2: mitigate bursty flows?
Testbed with P4-enabled Barefoot Tofino, 4 snapshots
Test: flow-based ECN, when “a flow is causing others to wait”
  Baseline: ECN all packets, when queue is long
100G
10G
Sender
Receiver
Send 1M TCP flows
+ synthetic bursts
Notes: BF switch
10G bottleneck
Sender sends 1M small&medium flows @ 20% utilization, also bursts.
P4 conquest + testbed ECN P4 program. Action: Whenever delay high, find out flows occupying large queuing space (alpha=25%) ECN those pkts.
(explain ECN)
Please refer to our paper for more detail.
end at 15:10

## Slide 20: Evaluation 2: mitigate bursty flows?
Flow-based ECN reduces Flow Completion Time
Queue remains short, bursty flow effectively suppressed
11%
Notes: Slower on both figures.
First figure: give highlight (reduce FCT by 11%), and then pause.
result similar for other Congestion Control in linux kernel, except BBR ignores ECN.
//(Now BBRv2 cares about ECN)
(Skip second figure, if no time.)
Second figure: introduce, give context, …
end at 16:30?

## Slide 21: Legacy network device not programmable
Not all network devices are programmable yet …
We need queuing analytics now!
Y U no ?
Notes: There's a problem:
P4 is not everywhere, yet!
Sad, but true...

## Slide 22: Legacy network device
Ingress
Ingress
Ingress
Not all network devices are programmable yet…
We need queuing analytics now!
Tap ingress + egress links
Record a packet’s appearances, analyze queuing delay
Ingress
Egress
Ingress
Egress
P
P
P
Packet P, flow ID F
Enqueued at t=20
P
Packet P, flow ID F
Dequeued at t=28
Notes: "on-demand queue debugging"
legacy switches, up and running in production
although cannot suppress in real time, we can measure better,
help operator understand queuing dynamics, find root cause
end at 18:00

## Slide 23: Evaluation 3: analyze legacy devices
Measured delay matches coarse-grained report
Result: >90% Precision & Recall
Deployed for queues in the wild
  Princeton P4Campus
  AT&T Labs
Notes: (Skip if no time.)
Let me quickly show some validations of the tapping setup.
Blue cross, GT queue length reported by legacy device, remind: 1/sec
Red line, per-packet queuing delay measured by P4 switch, match pretty well, except much more fine-grained.
P/R: similar, omit here.
ConQuest have been deployed in this manner to analyze real queues in today's production networks.
In Princeton's P4Campus initiative,
Found root cause of queuing anomalies in a campus border switch
at AT&T, our collaborators have used ConQuest to measure microbursts in carrier core network, and they have presented their result in last week's Buffer Sizing Workshop.
end before 19:00-19:30

## Slide 24: Image Credits
Uber waiting screenshot: techcrunch, mockuphone
Airport: flickr.com/photos/heathershacienda/199507247/ CC-BY 2.0
Smurfs:
  pngimg.com/download/47420 CC-BY-NC 4.0
  clipartmag.com/smurf-drawing#smurf-drawing-10.jpg CC-BY-NC 4.0
  imgur.com/gallery/cdvqgwa imgur.com/a/KcmQhj6 Imgur tos UGC NC
High latency Stadia gaming: washingtonpost
Soccer video: youtu.be/J0dICCF7B6A

## Slide 25: Summary, Q&A
ConQuest : round-robin snapshots in the data plane
Identify flows contributing to long queuing delay in real time
Reduce Flow Completion Time by up to 11% given bursty flows
Egress
Why am I waiting?
Notes: In summary,
1. Today we present ConQuest, a queue analysis data structure using RR Snap in the DP
2. ConQuest can identify flows contributing to long queuing delay, in REAL TIME, providing opportunity for immediate corrective action
3. By combining ConQuest with Advanced Queue Management (AQM), we can improve FCT by 11% when there are bursty flows in the network
With ConQuest, the smurf can finally answer with confidence: "why am I waiting in a long queue"?

## Slide 26: Backup slides

## Slide 27: Estimated / Real flow size

## Slide 28: Number of snapshots: 4 or 8

## Slide 29: Per-snapshot memory size

## Slide 30: Precision/Recall curve
Simulator
Testbed

## Slide 31: Hash Collision / Rounding